## Slide 1: PLUS 2.0 Architecture
Adam Rankin, Andras Lasso, Csaba Pinter, Tamas Ungi, and Gabor Fichtinger
Laboratory for Percutaneous Surgery (Perk Lab) School of Computing Queen’s University, Kingston, ON, Canada

## Slide 2
Glossary
Device
Channel
Data Source
Tag
Attribute
Tracked Frame
XML tag is an entry in an XML file: <Unicorn/>
XML attribute is a property of a tag <Unicorn realness=“notReal” size=12 />
Device (hardware) is any physical or virtual device
Hardware
Transform
Device (software) is our interface to a physical device
Channel is a logical construct representing a stream of data
Data source is a logical construct around a buffer containing meta information (what type of source, etc…)
Tracked frame is the result of merging multiple data sources into a data structure. Tracked frame = 1 video + N transforms
Transform is 4x4 matrix representing a transformation in 3-space (translation, rotation, scaling)

## Slide 3
PLUS Architecture Overview
hardware
Ultrasound scanner
Navigation system
Temporal calibration
Device
software
Interface
Algorithms
N-Wire calibration
Volume reconstruction
Single wall calibration
Line segmentation
Data
Tracked frame
Channel
Data sources
…
Developed in the Perk Lab
Developed by collaborators

## Slide 4
A Device
Hardware
Private
Developed in the Perk Lab
Developed by collaborators
Device interface
Public
Channels
Data sources
Transform data sources
Video data sources
Input Channels
Output Channels

## Slide 5
Pipeline
EM Tracker
Ultrasound
B-mode Channel
Channel
Rf-mode Channel
B Virtual Mixer
Rf Virtual Mixer
Rf Virtual Capture
B Virtual Capture
Data Flow
Channel
Channel
Visualization Client
Devices are the creation point of data
  Recorded data from world
  Simulated data, processed data
Channels are the communication point between devices
  Outputs tracked frames for client consumption

## Slide 6
Configuration Files
Linking input & output via channels
  Device -> channel -> device (repeat)
Channel contains data sources
  At most one video, many transforms
All connections made via ID matching
<Device
Id="TrackerDevice"
Type="Ascension3DG"
AcquisitionRate="50"
LocalTimeOffsetSec="0.0"
FilterAcWideNotch="1" >
<DataSources>
<DataSource Type="Tool" Id="Probe" PortName="0" />
<DataSource Type="Tool" Id="Reference" PortName="1" />
<DataSource Type="Tool" Id="Stylus" PortName="2" />
</DataSources>
<OutputChannels>
<OutputChannel Id="TrackerStream" >
<DataSource Id="Probe"/>
<DataSource Id="Reference"/>
<DataSource Id="Stylus"/>
</OutputChannel>
</OutputChannels>
</Device>
<Device
Id="VideoDevice"
Type="SonixVideo"
… >
<DataSources>
<DataSource Type="Video" Id="Video" PortName="B" PortUsImageOrientation="UF" />
</DataSources>
<OutputChannels>
<OutputChannel Id="VideoStream" VideoDataSourceId="Video"/>
</OutputChannels>
</Device>
<Device
Id="TrackedVideoDevice"
Type="VirtualMixer" >
<InputChannels>
<InputChannel Id="TrackerStream" />
<InputChannel Id="VideoStream" />
</InputChannels>
…
</Device>