## Slide 1: PLUS 2.0 Architecture
Adam Rankin, Andras Lasso, Csaba Pinter, Tamas Ungi, and Gabor Fichtinger
Laboratory for Percutaneous Surgery (Perk Lab) School of Computing Queen’s University, Kingston, ON, Canada

## Slide 2
Glossary
Device
Channel
Data Source
Tag
Attribute
Tracked Frame
XML tag is an entry in an XML file: <Unicorn/>
XML attribute is a property of a tag <Unicorn realness=“notReal” size=12 />
Device (hardware) is any physical or virtual device
Hardware
Transform
Device (software) is our interface to a device, using an SDK
Channel is a logical construct representing a stream of data
Data source is a logical construct around a buffer containing meta information (what type of source, etc…)
Tracked frame is the result of merging multiple data sources into a data structure. Tracked frame = 1 video + N transforms
Transform is 4x4 matrix representing a transformation in 3-space (translation, rotation, scaling)

## Slide 3
PLUS Architecture Overview
Hardware
Temporal calibration
Device
Algorithms
N-Wire calibration
Volume reconstruction
Single wall calibration
Line segmentation
Data
Tracked frame
Channel
Data sources
…
Device Specific SDK
Applications
fCal
PlusServer
iCal
…
Notes: This shows a layered approach to what depends on what
SDK – software development kit, functions to interact with a specific piece of hardware

## Slide 4
Inside A Device
Hardware
Internals
Device Specific SDK
Input
Output
A Channel
…
Data sources
Video data sources
Data Processing
A Channel
A Channel
Transform data sources
Notes: Demonstrate the logical structure of a device

## Slide 5
Pipeline
EM Tracker
Ultrasound
B-mode Channel
Channel
Rf-mode Channel
B Virtual Mixer
Rf Virtual Mixer
Rf Virtual Capture
B Virtual Capture
Data Flow
Channel
Channel
Visualization Client
Devices are the creation point of data
  Recorded data from world
  Simulated data, processed data
Channels are the communication point between devices
  Outputs tracked frames for client consumption
Notes: Explain what a mixer device is
Explain what a capture device is

## Slide 6
Configuration Files
Linking input & output via channels
  Device -> channel -> device (repeat)
Channel contains data sources
  At most one video, many transforms
All connections made via ID matching
<Device
Id="TrackerDevice"
Type="Ascension3DG"
AcquisitionRate="50"
LocalTimeOffsetSec="0.0"
FilterAcWideNotch="1" >
<DataSources>
<DataSource Type="Tool" Id="Probe" PortName="0" />
<DataSource Type="Tool" Id="Reference" PortName="1" />
<DataSource Type="Tool" Id="Stylus" PortName="2" />
</DataSources>
<OutputChannels>
<OutputChannel Id="TrackerStream" >
<DataSource Id="Probe"/>
<DataSource Id="Reference"/>
<DataSource Id="Stylus"/>
</OutputChannel>
</OutputChannels>
</Device>
<Device
Id="VideoDevice"
Type="SonixVideo"
… >
<DataSources>
<DataSource Type="Video" Id="Video" PortName="B" PortUsImageOrientation="UF" />
</DataSources>
<OutputChannels>
<OutputChannel Id="VideoStream" VideoDataSourceId="Video"/>
</OutputChannels>
</Device>
<Device
Id="TrackedVideoDevice"
Type="VirtualMixer" >
<InputChannels>
<InputChannel Id="TrackerStream" />
<InputChannel Id="VideoStream" />
</InputChannels>
…
</Device>
Notes: Emphasize the linkage by ID, give them a basis to understand other config files

## Slide 7
TrackerDevice
Examples: Simple Tracked Video
Internal data sources
Output Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
ProbeToTracker
ReferenceToTracker
StylusToTracker
MixerDevice
Output Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
Input Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
VideoDevice
Internal data sources
Output Channel
Video
Video
Input Channel
Video
Video

## Slide 8
TrackerDevice
Examples: RF/B-mode Acquisition
Internal data sources
Output Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
ProbeToTracker
ReferenceToTracker
StylusToTracker
MixerDevice
Output Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
Input Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
VideoDevice
Internal data sources
Output Channel
RfModeVideo
RfModeVideo
Input Channel
Video
Video
Output Channel
BModeVideo
BModeVideo
MixerDevice
Output Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
Input Channel
ProbeToTracker
ReferenceToTracker
StylusToTracker
Input Channel
Video
Video